## Slide 1: Halo 12 Memory Layout Change
Changes from PDR

## Slide 2: Original Memory Layout
Non-Volatile FRAM – 256KB
  Stores application binary
  Processor copies contents into SRAM on boot
Internal SRAM – 256KB for Program Memory
  Application execution area
  Extra room can be used for data memory
  200KB for Thruster Control Application
  56KB for Data – Trace Message Buffer
Internal SRAM – 64KB for Data Memory
  Used for Thruster Control Application stack
External SRAM – 2MB for Data Memory
  Thruster Control Application data memory
External NOR Flash – 64MB
  14MB for Application data
  Addition space can be utilized with a custom driver
14MB Application Data Area
  Layout of Thruster Control App, Update Image and Redundant copies is legacy carryover of Halo 6 which used rad-tolerant chips
  This was a safety measure in the event an area of memory got corrupted, then there would be backups
  VA41630 and the External NOR are rad-hard and can benefit from another strategy

## Slide 3: New Memory Layout
Files Changed
Storage_memory_layout.h
Storage_memory_file_map.c
Component_keys.h
Va416xx_linker_freertos.ld
Va416xx_linker_baremetal.ld
256k FRAM
256k int SRAM
0x00000000
64k int SRAM
0x1FFF8000
14MB ext Addressable
NOR Flash
(64MB device)
2MB ext SRAM
0x60000000
0x60E00000
SRAM1 (32k)
SRAM2 (30k)
RTT (2k)
Image Backup Region 2
Software Update Backups
Regions are 1MB each
Store images and headers for all three devices; ECPK, MVCP, ACP
App stores state for each region in the Application Data area
App Configuration Region
Application Configuration
Region is 65kB
Store configuration data required by app that must persist after power cycle
Image Backup Region 1
0x60000000
0x60100000
0x60200000
Data Region (1M)
SW Update
Region (1M)

## Slide 4: Software Update Binary
Update Image Header
ECPK Header
MVCP Header
ACP Header
ECPK Image
MVCP Image
ACP Image
Padding
256kB
256kB
256kB
256B
Target Magic Number
Offset within the update binary
Size of the image (region or actual)
Device ID (ECPK, MVCP, or ACP)
Firmware Major Version
Firmware Minor Version
Firmware Patch Version
Git SHA
Image CRC
Update Magic Number
Size of the update binary
Number of images (always 3)
ECPK Header
MVCP Header
ACP Header
Header Region CRC
Update Binary Contains Image For Each Device
  Typically the same image is deployed on each device and resistor population options determine behavior
  This structure allows different versions to be deployed
  Also allows dedicated firmware for each device
  If one image is to be deployed to all three devices then only one image is included and all headers point to this image
Update Image Header
  First 256B of Update Binary
  Metadata about the whole region
  Encompasses the image headers
  CRC is for the whole region
Device Headers
  Each one is 64B
  Metadata about the Image
  CRC is for the image

## Slide 5: ECPK Software Update Process
Upload from FCP
Index = 0x5500
Sub-index = 0x01
Write update image to update binary region of SRAM
Check CRC’s when complete
Verify Upload (w)
Index = 0x5500
Sub-index = 0x02
Decrypt (future)
Verify CRC’s
Read Result (r)
Index = 0x5500
Sub-index = 0x02
Install
Index = 0x5500
Sub-index = 0x03
Write the update image to NOR Flash
Write ECPK image to FRAM
Send the MVCP image to the MVCP device
Send the ACP image to the ACP device
Application Data Region
Update Binary Region
Image Backup Region 1
Header
ECPK Image
MVCP Image
ACP Image
Update Binary
EBI NOR Flash
Image Backup Region 2
FRAM
ECPK Image
Enable
Index = 0x5500
Sub-index = 0x04
Resets all devices
Causes FRAM images to be read into program memory
EBI SRAM (volatile)
EBI NOR Flash (non-volatile)
Update Binary Region
Header
%&#@ Image
*@%^ Image
&*^& Image
Update Binary
Application Data Region
Application Data - TBD
Image Backup Region 2
0x60100000
Image Backup Region 1
0x60000000
FRAM
0x00000000
0x60E00000
0x60F00000
0x60200000
FRAM
Application Data Region
Update Binary Region
Header
ECPK Image
MVCP Image
ACP Image
Update Binary
Application Data - TBD
Image Backup Region 2
Image Backup Region 1
Question
If installing without a valid image in SRAM, do we copy the active or stale backup region?
Doing stale allows to go back to a previous release.
Doing active just reloads the image currently in FRAM.

## Slide 6: ECPK Software Update Process Detail
Verify Upload (w)
Index = 0x5500
Sub-index = 0x02
Image Backup Regions
Two regions to store images for each of the three devices (ECPK, MVCP, ACP).
Each region is 1MB = 16 sectors (smallest erase is a 65kB sector)
Each region has two states; stale and active
Active = has been written to FRAM. Only one region can be active at a time, the other must be stale
When an update is received it is validated as it is transferred to the stale backup region
Once the full update image is transferred it remains stale until user sends Install command
The user sends a Install command to make the update active and copy it to FRAM
The user can use the Install command to switch back and forth between the latest and the previous versions
Initialize both regions as stale. If someone attempts to install we will fail
Region 1 State?
Write Image to Region 1
Write Image to Region 2
Region 2 = stale
Stale
Active
Install
Index = 0x5500
Sub-index = 0x03
Region 1 State?
Check Region 1 CRC
Stale
Active
Region 1 = Active
Region 2 = Stale
Pass?
Yes
No
Check Region 2 CRC
Send Region 2 Images to Clients
Pass?
Yes
No
Always check region 1 first
Copy Region 2 image to FRAM
Region 1 = Stale
Region 2 = Active
Send Region 1 Images to Clients
Copy Region 1 image to FRAM
Installs what is in a stale region and makes it active, IF, there is a valid image in the stale region.
End
1
2
Fail
Upload an update
Fail
Upload an update
End